## Slide 1: 2023 Laufer Energy Symposium Unconventional Fuels
Vivek M Rao, PhD
Fusion and Fission Energy and Science Directorate, ORNL
March 30, 2023

## Slide 2: Motivation
“ hybrids producing thermal energy, hydrogen, or other renewable fuels can specifically target hard to decarbonize applications in the industrial and transportation sectors, which can provide significant additional GHG reductions required to achieve a net-zero economy by 2050”
“ competitively selected projects apply modeling, simulation, and data analysis to industrial processes and products to lower production costs and shorten the time to market. The aim is to advance future technology investments by optimizing designs, predicting performance, and reducing the number of testing cycles during development “
Office of Energy Efficiency and Renewable Energy
Office of Advanced Manufacturing
And Industrial Decarbonization
Office of Energy Efficiency and Renewable Energy
“In the U.S., there are approximately 40,000 commercial vessels and 360 commercial seaports handling every type of cargo, from people to phosphorus. There are an additional 10.5 million motorized recreational boats”
“Global emissions from all vessels account for about 3% of total GHG emissions each year; if the maritime industry was its own country, it would rank sixth on the list of largest GHG emitters globally.”
Hybrid energy systems, why?
How to leverage super computing resources?
Why decarbonize the maritime industry?

## Slide 3: Initiatives by USDOE
https://www.energy.gov/policy/energy-earthshots-initiative

## Slide 4: Key Challenges in Fuel-to-Energy
Nuclear Processes
Thermal Transport Processes
Biofuel Processes
Solar Power Systems
Nuclear fission
Nuclear fusion
Beams
Plasmas
Multiphase interactions
Flow regime dynamism
Flow stratification
Reacting flows, phase change
Material behavior
Air-fuel pre-heat
Oxidation
Radiation
Refractory wear
Emissions enthalpy
Optical configuration, accumulation of heat
Removal and storage of heat (concentrated solar power)
Power block design
Reduced Order Models, Experiments, V&V, Benchmarks, Materials Response, Life-Cycle, Techno-Economic Feasibility, Commercialization
Sustainable Transportation
BETO
HFTO
VTO
Waste Heat Recovery
Sensible heat recovery
Balance-of-plant
Sequestered heat

## Slide 5: Computational Design Workflows for Modular Power
Multiphysics Modeling and Simulation
Flow Regimes
Transport Phenomena
Fluid-Structure Interactions
Thermal Hydraulics
Concentrated Solar Power
Offshore Wind Power
Sustainable Transportation
Energy sectors which can benefit from technology development in modular nuclear power
Inertial flows
Process scaleup
f(T,P)
f(P, T)wall
Powerful CAE Design Tools
High-Performance Computing Resources
Advanced Manufacturing Techniques
Probabilistic Risk Assessment and Process Safety
Tech
to
Market
Lessons Learned from Nuclear Technology

## Slide 6: Unique Capabilities at ORNL: Molten Salt (Fluoride) Test Loop
Yoder G. Liquid Salt Test Loop Fact Sheet. 2016.
https://www.energy.gov/eere/articles/concentrating-solar-power-could-provide-flexibility-and-reliability-us-electric-grid

## Slide 7: Unique Capabilities at ORNL: Molten Salt (Chloride) Test Loop
ORNL/TM-2019/1370. Facility to Alleviate Salt Technology Risks (FASTR): Preliminary Design Report with Failure Modes and Effects Analysis. Robb K, Mulligan P, Yoder G, Smith K and Massengale J. 2019.

## Slide 8: Unique Capabilities at ORNL: Fusion Science
Original artwork reproduced with permission, from “Juergen Rapp, Arnold Lumsdaine, Clyde Beers, Theodore Biewer, Timothy Bigelow, Ted Boyd, Juan Caneses, John Caughman, Robert Duckworth, Richard Goulding, William Hicks, Cornwall Lau, Pawel Piotrowicz, David West, Dennis Youchison, The Material Plasma Exposure eXperiment: Mission and conceptual design, Fusion Engineering and Design, Volume 156, 2020, 111586, ISSN 0920-3796”.
Material Plasma Exposure eXperiment (MPEX)

## Slide 9: Thermal Efficiency Improvements 1. Direct-Contact Heat Exchanger for Low-Temperature Waste Heat Recovery

## Slide 10: Immiscible Water-Refrigerant Mixture
Volume
Fraction
Of Pentane(l)
7-nozzle 19-nozzle 36-nozzle
Volume
Fraction

## Slide 11: Multiphysics Model Development

## Slide 12: Multiphysics Model Validation
= 0.05 = 0.10 = 0.15 = 0.20
1.3x COARSE
BASE MESH
1.3x FINE
BASE MESH
Measured value ~ 16.75 cm
= 0.014
= 0.014
= 0.025
7-nozzle Sparger:
Sensitivity
of predicted
active heights
to global mesh
refinement

## Slide 13: Prediction of Steady Operation
Water
Jet
Pentane(l)

## Slide 14: Validated Model to New Design
Notes: Best-case energy savings: 251M BTU per year for simulated design
Practical design would save 25.1 BBTU per year, or roughly the consumption of 500 tonnes of kerosene

## Slide 15: Thermal Efficiency Improvements 2. Additively Manufactured Ceramics for High-Temperature Gas-to-Gas Operations

## Slide 16: High-Temperature Composite Heat Exchangers
Shell-Side
Mass Inflow 0.265 kg/s
Inlet Temperature 1150.0 K
Tube-Side
Mass Inflow 0.2735 kg/s (total)
Inlet Temperature 421 K
Simulated rate of heat transfer to tube-side (cold fluid): 2.2 kW
Ceramic Coils
ΔP (1 tube) < 0.3 psi
Fluid Profile
55M cells
(tube array)

## Slide 17: High-Temperature Composite Heat Exchangers
Consistency in flow – plume length, span-wise temperature, pressure
No stagnation of flow near “walls”
ΔP ~ 0.03 psi

## Slide 18: High-Temperature Composite Heat Exchangers
 | Simulated Rate of Heat Transfer, Q (W) |  | Q/V (kW/m3) |  | Q/ΔP (kW/psi) | 
 | Spiral Array | Gyroid Plate | Spiral Array | Gyroid Plate | Spiral Array | Gyroid Plate
SUNY Anode | 29.75 | 3378 | 7.65 | 4263 | 1.65 | 3246
SUNY Cathode | 2200 | 50944 | 343 | 64290 | 0.31 | 77
Brayton Energy | 24.10 | 914 | 6.2 | 1153 | 1.04 | 1974
CSM Fuel-Side | 21158 | 9500 | 3295 | 11989 | 7.78 | 272
CSM Air-Side | 22600 | 10149 | 3520 | 12808 | 18.06 | 400

## Slide 19: Thermal Map: Power Density and Pressure Drop
Chart: Rate of Heat Transfer per Volume of Solid (W/m3) vs. Total Pressure Drop (psid)
| 8.5000000000000006E-2 | 0.11700000000000001 | 0.19 | 0.42199999999999999
W/m3 | 9082397.0037 | 8008051.5298 | 11447347.5851 | 10147881.6946

## Slide 20: Thermal Map: Specific Power Density and Wall Thickness
Chart: Estimated Gradients of Heat Transfer: Wall Thickness (in.) and Angular Frequency (π)
W/kg | 3129.0323 | 2762.7778 | 3950.2732 | 3494.0367
2pi, 0.05”
2pi, 0.075”
3pi, 0.075”
2379 W/π
2644 W/π
4920 W/in.
15520 W/in.

## Slide 21: Thermomechanical Summary
 |  | Pin (psig) | ΔP (psid) | Rate of Heat Transfer (W) | Mass of Solid Walls (kg) | Volume of Solid Wall (m3) | Tin (oC) | Tout (oC) | Principal Stress (Pa) | Max. Displac-ement (µm)
2pi 0.05” | Hot | 0.032 | 0.053 | 4850 | 1.55 | 5.34e-4 | 619 | 553 | < 25 MPa | 437
 | Cold | 0.019 | 0.032 |  |  |  | 267 | 343 |  | 
2pi 0.075” | Hot | 0.043 | 0.076 | 4973 | 1.80 | 6.21e-4 | 619 | 548 | < 25 MPa | 543
 | Cold | 0.033 | 0.041 |  |  |  | 267 | 342 |  | 
3pi 0.050” | Hot | 0.011 | 0.126 | 7229 | 1.83 | 6.315e-4 | 619 | 517 | < 25 MPa | 244
 | Cold | 0.055 | 0.064 |  |  |  | 267 | 370 |  | 
3pi 0.075” | Hot | 0.178 | 0.284 | 11961 | 2.18 | 7.506e-4 | 619 | 453 | < 25 MPa | 168
 | Cold | 0.304 | 0.138 |  |  |  | 267 | 354 |  | 
CFD-informed FEA Predictions

## Slide 22: Developing the Gyroid
Cold
Flow
Hot
Flow
Shell-Side (Hot Fluid)
Flow Rate 0.04502 kg/s
Inlet Temperature 619 C (892.16 K)
Tube-Side (Cold Fluid)
Mass Inflow 0.034668 kg/s (total)
Inlet Temperature 267 C (540.16 K)
(Colorado School of Mines)
NECTAR Design

## Slide 23: CAD to Realization
Cold
Flow
IN
Closed to
Both Fluids
Cold
Flow
OUT
Closed to
Both Fluids
Hot
Flow
OUT
Hot
Flow
IN
Printed at ORNL Manufacturing
Demonstration Facility

## Slide 24: Gas to Gas HX: Flow Volumes
COLD
FLUID
HOT
FLUID
IN
OUT
IN
OUT

## Slide 25: High-Temperature Composite Heat Exchangers
2pi, 0.05”
2pi, 0.1”
4pi, 0.1”
3pi, 0.05”
4pi, 0.05”

## Slide 26: High-Temperature Composite Heat Exchangers
Chart: Gyroid Core - Basis
| 26756 | 11388 | 18714 | 3839 | 3006
W/kg (gy) | 2692.9032 | 3369.5876 | 3464.2857 | 1153.4483 | 2192.0139
Chart: Heat Exchanger - Basis
| 26756 | 11388 | 18714 | 3839 | 3006
W/kg (tot) | 381.5356 | 576.455 | 525.7453 | 235.3355 | 514.0879
Chart: Power (W) vs. Mass of Gyroid Core (kg)
| 1.55 | 1.94 | 1.68 | 2.3199999999999998 | 2.88
Power (W) | 4174 | 6537 | 5820 | 2676 | 6313
2pi, 0.05”
2pi, 0.1”
4pi, 0.1”
3pi, 0.05”
4pi, 0.05”
2pi, 0.05”
2pi, 0.1”
4pi, 0.1”
3pi, 0.05”
4pi, 0.05”
2pi, 0.05”
2pi, 0.1”
4pi, 0.1”
3pi, 0.05”
4pi, 0.05”
Chart: Power (W) vs. System Pressure Drop (psid)
| 0.156 | 0.57399999999999995 | 0.311 | 0.69699999999999995 | 2.1
Power (W) | 4174 | 6537 | 5820 | 2676 | 6313
4pi, 0.05”
2pi, 0.05”
3pi, 0.05”
2pi, 0.1”
4pi, 0.1”

## Slide 27: Ongoing Research
Heat exchangers w/ invertible Leidenfrost dynamics (ARPA-e CREATE)
Micro-HTGR in PCC conditions (NEUP)
Cymatic fluid dynamics
Pumped storage hydro power (WPTO HydroWIRES)
Tandem wind-tidal-wave energy capture ORBs for offshore marine power (WPTO Marine Energy Seedlings)

## Slide 28: Support from Wayne and Gayle Laufer Endowment

## Slide 29: Nuclear Energy | SMR | Lower Plenum
Westinghouse Nuclear – Small Modular Reactor (WSMR)
Based on the AP-1000 design (1100 MWe)
Advanced passive safety features
Cool operation w/o human intervention or AC power for 7 days
Design life: 60 years
Integral pressurizer unit
Integral annular steam-generator unit
Total site area ~ 15 acres
Rail, truck, or barge shippable
Underground containment
Containment cooling via evaporation, condensation, gravity
Reactor core thermal output: 800 MW
Active fuel length: 8 ft (~2.4 m)
Less than 5% enriched UO2 fuel
17x17 robust fuel assemblies (RFAs)
89 fuel assemblies
37 internal CRDMs
100,000 gpm coolant flow rate
8 reactor coolant pumps (RCPs)
3.5 m ∅ reactor pressure vessel (RPV)
24.1 m height RPV
Secondary side heat to 225 MWe
Concept Thermal Design
Image Courtesy: Westinghouse. ©2020 Westinghouse Electric Company LLC. All rights reserved.

## Slide 30: Nuclear Energy | SMR | Lower Plenum

## Slide 31: Nuclear Energy | SMR | Lower Plenum
Chart: Y co-ordinate (m)
| -1.5 | -1.44 | -1.38 | -1.32 | -1.26 | -1.2 | -1.1399999999999999 | -1.08 | -1.02 | -0.96 | -0.89999999999999902 | -0.84 | -0.78 | -0.72 | -0.65999999999999903 | -0.6 | -0.54 | -0.48 | -0.41999999999999899 | -0.35999999999999899 | -0.29999999999999899 | -0.24 | -0.17999999999999899 | -0.119999999999999 | -0.06 | 0 | 0.06 | 0.12 | 0.18 | 0.23999999999999899 | 0.29999999999999899 | 0.35999999999999899 | 0.41999999999999899 | 0.48 | 0.54 | 0.59999999999999898 | 0.66 | 0.71999999999999897 | 0.78 | 0.83999999999999897 | 0.9 | 0.96 | 1.02 | 1.08 | 1.1399999999999999 | 1.2 | 1.26 | 1.3199999999999901 | 1.38 | 1.44 | 1.5
S-A | 1.756 | 2.7963 | 0.93732 | 2.7045 | 3.6744 | 4.3917 | 4.4077 | 4.4873 | 4.5192 | 3.9374 | 2.4678 | 3.3277 | 2.8468 | 2.4605 | 2.5168 | 2.4242 | 2.4597 | 2.5528 | 2.5115 | 1.6305 | 1.5309 | 1.8374 | 1.9598 | 1.9141 | 1.7913 | 1.7118 | 1.9464 | 1.6916 | 1.7818 | 1.8163 | 1.7042 | 1.4567 | 1.7002 | 2.3912 | 2.6998 | 2.7588 | 2.8961 | 2.9805 | 3.1486 | 3.3784 | 3.6392 | 3.0628 | 3.9038 | 4.1642 | 2.7561 | 3.1475 | 3.1251 | 2.8423 | 1.9932 | 3.7105 | 1.6316
k-omega | 0.92626 | 3.9952 | 1.4573 | 1.4595 | 1.1613 | 1.2171 | 1.0954 | 1.4796 | 2.0719 | 2.3997 | 3.0037 | 2.7471 | 2.9562 | 3.0066 | 2.9218 | 2.7574 | 2.6034 | 2.5712 | 2.4826 | 2.2965 | 2.2381 | 2.199 | 2.1985 | 2.2779 | 2.2962 | 2.0892 | 1.7656 | 1.9124 | 2.2854 | 2.3953 | 2.8978 | 2.364 | 2.4943 | 2.8115 | 2.4386 | 2.4111 | 2.522 | 2.2844 | 3.573 | 3.5888 | 3.9875 | 3.3657 | 3.4012 | 4.4151 | 4.6139 | 3.7709 | 3.3705 | 2.535 | 1.8955 | 1.1952 | 2.184
k-eps | 0.29185 | 3.3523 | 1.0029 | 1.7613 | 1.4618 | 0.98205 | 1.0453 | 1.6178 | 2.1343 | 2.5294 | 2.8378 | 2.8497 | 2.6348 | 2.5148 | 2.3509 | 2.2355 | 2.1716 | 2.2627 | 2.2471 | 2.1131 | 2.0266 | 1.7636 | 1.5445 | 1.4614 | 1.6415 | 1.9385 | 2.1003 | 2.1092 | 2.0758 | 1.9619 | 1.7498 | 1.7652 | 1.8466 | 1.9825 | 2.3434 | 2.5695 | 2.8041 | 2.9166 | 3.2613 | 3.6191 | 3.9358 | 4.035 | 3.7627 | 3.6237 | 3.7074 | 3.7492 | 3.4544 | 2.5489 | 1.194 | 4.3494 | 0.51664
RST | 0.51308 | 2.5277 | 1.7962 | 2.4447 | 2.8942 | 3.0527 | 3.0239 | 2.935 | 2.8563 | 2.8845 | 3.0963 | 3.1007 | 3.0123 | 2.9913 | 2.8756 | 2.7526 | 2.6473 | 2.5268 | 2.3555 | 2.0121 | 1.9001 | 1.8068 | 1.7252 | 1.6988 | 1.8283 | 1.9251 | 1.8011 | 1.6567 | 1.7726 | 2.0217 | 2.2877 | 2.4334 | 2.5575 | 2.6512 | 2.6305 | 2.6561 | 2.8265 | 2.9662 | 3.0496 | 3.1306 | 3.0797 | 2.8759 | 2.8428 | 2.9017 | 2.9577 | 3.0221 | 2.9238 | 2.4671 | 1.6865 | 2.4572 | 0.53771
Chart: Y co-ordinate (m)
| -1.38 | -1.32 | -1.26 | -1.2 | -1.1399999999999999 | -1.08 | -1.02 | -0.96 | -0.89999999999999902 | -0.84 | -0.78 | -0.72 | -0.65999999999999903 | -0.6 | -0.54 | -0.48 | -0.41999999999999899 | -0.35999999999999899 | -0.29999999999999899 | -0.24 | -0.17999999999999899 | -0.119999999999999 | -0.06 | 0 | 0.06 | 0.12 | 0.18 | 0.23999999999999899 | 0.29999999999999899 | 0.35999999999999899 | 0.41999999999999899 | 0.48 | 0.54 | 0.59999999999999898 | 0.66 | 0.71999999999999897 | 0.78 | 0.83999999999999897 | 0.9 | 0.96 | 1.02 | 1.08 | 1.1399999999999999 | 1.2 | 1.26 | 1.3199999999999901 | 1.38
S-A | 1.2815 | 2.5289 | 2.7702 | 3.2752 | 3.5402 | 3.7546 | 3.5773 | 2.9867 | 2.7568 | 2.4419 | 2.2033 | 2.5142 | 2.9695 | 2.7026 | 2.0369 | 1.8689 | 2.3232 | 2.6258 | 2.3501 | 1.6995 | 1.1762 | 1.3329 | 1.1737 | 0.91912 | 1.0525 | 1.1992 | 1.5755 | 1.8692 | 1.9273 | 0.63013 | 0.83767 | 1.0652 | 1.1952 | 1.6944 | 2.0985 | 2.3722 | 2.8039 | 3.0452 | 3.3813 | 3.7395 | 3.8462 | 3.664 | 3.4058 | 3.2115 | 3.0607 | 2.8767 | 3.0131
k-omega | 2.2823 | 2.3745 | 2.6323 | 3.1701 | 3.4217 | 3.66 | 3.7859 | 3.7476 | 3.3183 | 2.9186 | 2.8674 | 2.6608 | 2.6047 | 2.8434 | 3.1826 | 3.2617 | 3.095 | 2.5804 | 2.2856 | 2.0753 | 1.8747 | 1.5058 | 1.3629 | 1.3004 | 1.3867 | 1.4555 | 1.4758 | 1.4557 | 1.5669 | 1.8671 | 1.8556 | 1.53 | 1.319 | 1.3641 | 1.632 | 2.2302 | 2.7078 | 3.0855 | 3.1194 | 2.2431 | 1.9295 | 2.1475 | 2.2822 | 2.3235 | 1.7974 | 1.1512 | 1.3218
k-eps | 1.8919 | 2.0328 | 2.273 | 2.8019 | 3.1086 | 3.4253 | 3.5974 | 3.6413 | 3.5708 | 3.4788 | 3.2911 | 3.1844 | 3.0277 | 2.9083 | 2.7769 | 2.7946 | 2.8003 | 2.6126 | 2.3629 | 1.6055 | 1.1826 | 1.3258 | 1.7011 | 2.032 | 2.2037 | 2.2312 | 2.0893 | 2.0113 | 1.9156 | 1.5861 | 0.9889 | 0.14966 | 1.2413 | 1.9986 | 2.728 | 2.8293 | 2.7231 | 2.6835 | 2.6789 | 2.8249 | 3.1209 | 3.1101 | 2.9564 | 3.2233 | 3.5298 | 3.689 | 3.9236
RST | 1.7352 | 1.8715 | 2.182 | 2.7649 | 3.0898 | 3.418 | 3.5516 | 3.4896 | 3.2388 | 3.062 | 2.796 | 2.7026 | 2.6422 | 2.6217 | 2.5436 | 2.2467 | 1.8821 | 1.0595 | 0.76384 | 1.2296 | 1.7409 | 1.8469 | 1.8401 | 1.8171 | 1.8188 | 1.8013 | 1.6024 | 1.1744 | 0.88178 | 1.4578 | 2.1599 | 2.5911 | 2.6984 | 2.6851 | 2.6404 | 2.6496 | 2.8364 | 3.0373 | 3.2915 | 3.4478 | 3.4961 | 3.403 | 3.1196 | 2.5999 | 2.1597 | 1.8768 | 1.6233
Chart: Y co-ordinate (m)
| -1.2 | -1.1399999999999999 | -1.08 | -1.02 | -0.96 | -0.89999999999999902 | -0.84 | -0.78 | -0.72 | -0.65999999999999903 | -0.6 | -0.54 | -0.48 | -0.41999999999999899 | -0.35999999999999899 | -0.29999999999999899 | -0.24 | -0.17999999999999899 | -0.119999999999999 | -0.06 | 0 | 0.06 | 0.12 | 0.18 | 0.23999999999999899 | 0.29999999999999899 | 0.35999999999999899 | 0.41999999999999899 | 0.48 | 0.54 | 0.59999999999999898 | 0.66 | 0.71999999999999897 | 0.78 | 0.83999999999999897 | 0.9 | 0.96 | 1.02 | 1.08 | 1.1399999999999999 | 1.2
S-A | 0.91282 | 0.44333 | 1.5821 | 1.4309 | 1.492 | 1.6347 | 1.319 | 0.44824 | 0.37896 | 0.43263 | 0.3974 | 0.2765 | 0.35704 | 0.49207 | 0.94797 | 1.2175 | 1.1933 | 1.2612 | 1.4447 | 1.574 | 1.7597 | 1.9956 | 2.116 | 1.988 | 1.5265 | 0.82852 | 0.62767 | 0.69506 | 0.6559 | 0.75786 | 1.0249 | 0.68033 | 0.80836 | 1.6017 | 1.678 | 1.6711 | 1.322 | 0.89107 | 0.88017 | 1.4001 | 0.76644
k-omega | 0.90802 | 1.4593 | 0.60199 | 0.88647 | 0.65613 | 0.57026 | 0.56485 | 0.65344 | 0.8211 | 0.76812 | 0.74562 | 0.70416 | 0.54886 | 0.48872 | 0.36878 | 0.2056 | 0.37521 | 0.72691 | 1.4317 | 1.7349 | 1.8457 | 1.5396 | 1.2999 | 1.1432 | 1.2592 | 1.1594 | 0.3201 | 0.55777 | 0.72493 | 1.2602 | 2.0714 | 2.1114 | 1.7574 | 1.0643 | 0.86795 | 0.74242 | 0.70589 | 0.71712 | 0.70839 | 1.4334 | 0.86283
k-eps | 0.98401 | 2.1562 | 0.85278 | 0.66043 | 0.32617 | 0.3249 | 0.3719 | 0.37445 | 0.36161 | 0.43767 | 0.65088 | 0.96179 | 0.97658 | 0.93137 | 0.7942 | 0.80132 | 1.2657 | 1.5988 | 2.0181 | 2.0984 | 2.1209 | 2.1641 | 2.0476 | 1.773 | 1.7455 | 1.6165 | 0.36484 | 0.80102 | 1.2968 | 1.7182 | 1.909 | 1.6671 | 1.2027 | 0.94917 | 0.81261 | 0.67289 | 0.69118 | 0.64704 | 0.57218 | 2.9746 | 1.6447
RST | 0.69591 | 1.3564 | 0.74762 | 0.56739 | 0.3965 | 0.26233 | 0.27077 | 0.14068 | 0.19029 | 0.73843 | 1.1326 | 0.78167 | 0.25965 | 0.092198 | 1.0352 | 1.5816 | 1.6745 | 1.7027 | 1.6223 | 1.5524 | 1.4673 | 1.5332 | 1.5959 | 1.627 | 1.6186 | 1.5661 | 0.72288 | 0.28062 | 0.31283 | 0.81366 | 1.2266 | 0.7452 | 0.2202 | 0.17555 | 0.2551 | 0.26688 | 0.39214 | 0.67896 | 0.88759 | 2.054 | 1.0019
Chart: Y co-ordinate (m)
| -0.89999999999999902 | -0.84 | -0.78 | -0.72 | -0.65999999999999903 | -0.6 | -0.54 | -0.48 | -0.41999999999999899 | -0.35999999999999899 | -0.29999999999999899 | -0.24 | -0.17999999999999899 | -0.119999999999999 | -0.06 | 0 | 0.06 | 0.12 | 0.18 | 0.23999999999999899 | 0.29999999999999899 | 0.35999999999999899 | 0.41999999999999899 | 0.48 | 0.54 | 0.59999999999999898 | 0.66 | 0.71999999999999897 | 0.78 | 0.83999999999999897 | 0.9
S-A | 1.99 | 1.7762 | 1.7957 | 1.9174 | 1.797 | 1.5614 | 1.2823 | 1.2127 | 1.2891 | 1.4482 | 1.5084 | 1.5319 | 1.5476 | 1.641 | 1.7122 | 1.7588 | 1.3909 | 1.0498 | 1.0309 | 1.264 | 1.4687 | 1.5437 | 1.4903 | 1.2564 | 1.1193 | 1.26 | 1.5464 | 1.7178 | 1.7367 | 1.6265 | 1.3881
k-omega | 1.7768 | 1.785 | 1.705 | 1.5797 | 1.4866 | 1.4265 | 1.5518 | 1.8367 | 2.0063 | 2.1619 | 2.1137 | 2.0067 | 1.9995 | 2.0467 | 2.035 | 2.0073 | 1.5453 | 0.63419 | 1.0542 | 1.685 | 1.5542 | 1.4279 | 1.6526 | 1.3794 | 0.9757 | 0.64098 | 0.21698 | 0.17826 | 0.60428 | 0.927 | 1.7366
k-eps | 2.5246 | 2.6611 | 2.6341 | 2.566 | 2.4966 | 2.4874 | 2.4937 | 2.5028 | 2.5017 | 2.4901 | 2.4761 | 2.4158 | 2.3178 | 2.0495 | 1.9006 | 1.693 | 1.5261 | 0.98496 | 1.238 | 1.3979 | 1.3981 | 1.4793 | 1.3589 | 1.0636 | 0.62606 | 0.42494 | 0.38088 | 0.5497 | 0.8911 | 1.2631 | 2.1839
RST | 1.8682 | 1.8936 | 1.8599 | 1.7934 | 1.6398 | 1.5479 | 1.4453 | 1.3891 | 1.4132 | 1.4872 | 1.4935 | 1.4318 | 1.2104 | 0.61122 | 0.51241 | 0.40121 | 0.45642 | 0.63303 | 1.1916 | 1.3534 | 1.4347 | 1.4416 | 1.4003 | 1.3877 | 1.4788 | 1.5608 | 1.6858 | 1.8146 | 1.9645 | 2.0559 | 2.094
1.
2.
3.
4.
Coefficient of Variation | Spalart-Allmaras | k-epsilon | k-omega | RST
z = -0.508 m | 0.166 | 0.424 | 0.378 | 0.326
z = -0.762 m | 0.473 | 0.568 | 0.504 | 0.654
z = -1.016 m | 0.389 | 0.321 | 0.331 | 0.321
z = -1.27 m | 0.340 | 0.397 | 0.333 | 0.252

## Slide 32: Nuclear Energy | SMR | Lower Plenum
RST
LES
Cut-off Frequency
LES successful in capturing sub-range of spatial frequencies corresponding to inertial forces in turbulent flow
TKE (J/kg)

## Slide 33: Nuclear Energy | SMR | Pressurizer Design
Image Courtesy: Westinghouse. ©2020 Westinghouse Electric Company LLC. All rights reserved.
10,278,437 hexahedral cells
Operating Pressure | 2250 psia
Inlet Velocity | 11.92 m/s
Steam Volume | 19.435 m3
Steam-Water Volumetric Ratio | ~1.5:1
Gravity | [0, 0, -9.81] m/s2

## Slide 34: Nuclear Energy | SMR | Prediction of Steam Quality
Design Data
9,188 tubes
60% steam quality – secondary side
Simulation Data
Primary Side Flow:
12 m/s into upper tube sheet
@ 605 K, 15.5 MPa;
Secondary Side Flow:
5.5 MPa
T_sat = 543.3 K
VOF Boiling (Rohsenow) model RST model used to simulate turbulent flow
Tube Side: 198.5M cells
Shell Side: 93.5M cells
30o sector of steam generator

## Slide 35: Nuclear Energy | SMR | Predicting Flow Under Pressurizer

## Slide 36: Nuclear Energy | SMR | Prediction of Steam Quality
90 Sector
Outlet averaged quality: ~87%
Profiles on Shell-Side Symmetry Plane
100 kg/s, 500 K @ Inlet
Profiles on Tube-Side Walls

## Slide 37: Nuclear Energy | SMR | Prediction of Steam Quality
90 Sector
Outlet averaged quality: ~67%
Profiles on Shell-Side Symmetry Plane
500 kg/s, 500 K @ Inlet
Profiles on Tube-Side Walls

## Slide 38: Acknowledgements
Wayne and Gayle Laufer Endowment
Missouri University of Science & Technology
Nuclear Energy and Fuel Cycle Division, ORNL
Fusion Energy Division, ORNL
Compute and Data Environment for Sciences (CADES), ORNL
USDOE Funding (NE, EERE, WPTO, ARPA-e)

## Slide 39: Thank you!
https://dilbert.com/strip/1989-09-24